apb_adv_timer Sub-System DV Architecture Specifications

Generated 2023/12/6

Copyright 2023
Datum Technology Corporation

# Description
APB Advanced Timer
# Design Under Test
## Design Element
Name	Type	Source
apb_adv_timer	fsoc	core-v-mcu

## Clocks
Name	Frequency	Signal Name	Description
sys_clk	100000000 Hz	HCLK	System
low_speed_clk	50000000 Hz	low_speed_clk_i	Low speed

## Resets
Name	Clock	Signal Name	Description
sys_reset	sys_clk	HRESETn	System

## Probe Signals
Name	Direction	Size	Clock	Reset	Description
dft_cg_enable_i	in	1	sys_clk	sys_reset	Design-for-test enable
ext_sig_i	in	32	sys_clk	sys_reset	External signal

# Block Environment Instances
## adv_timer0
Advanced timer 0
IP	Active/Passive	HDL Path
adv_timer	Passive	u_tim0

## adv_timer1
Advanced timer 1
IP	Active/Passive	HDL Path
adv_timer	Passive	u_tim1

## adv_timer2
Advanced timer 2
IP	Active/Passive	HDL Path
adv_timer	Passive	u_tim2

## adv_timer3
Advanced timer 3
IP	Active/Passive	HDL Path
adv_timer	Passive	u_tim3

# Agent Instances
## proc
Processor access
IP	apb
Active/Passive	Active
Mode	Normal
Clock	sys_clk
Reset	sys_reset
Memory Map	default
HDL Path	{{ name.upper() }}

### Configuration
Knob	Value
data_width	32
addr_width	32

# Common Test Configuration Knobs
Name	CLI Arg	Type	Description
selected_reg_block	REG_BLOCK	Register Block	Register block selected for register testing.

# Tests
Note: Automated register tests (ex: reg_bit_bash) are omitted for brevity.