apb_timer_ss Registers & Memories

Generated 2023/12/6

Copyright 2023
Datum Technology Corporation
# Parameters
Word size: 32
Endianness: little
# Registers
## cfg_reg_low - 0x0
1 = 64-bit mode, 0=32-bit mode
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:31	mode_64_bit	RW	1	True	x00	1 = 64-bit mode, 0=32-bit mode
30:30	mode_mtime_bit	RW	1	True	x00	1=MTIME mode Changes interrupt to be >= CMP value
14:8	prescaler_count	RW	7	True	x00	Prescaler divisor
7:7	ref_clk_en_bit	RW	1	True	x00	1= use Refclk for counter, 0 = use APB bus clk for counter
6:6	prescaler_en_bit	RW	1	True	x00	1= Use prescaler 0= no prescaler
5:5	one_shot_bit	RW	1	True	x00	1= disable timer when counter == cmp value
4:4	cmp_clr_bit	RW	1	True	x00	1=counter is reset once counter == cmp, 0=counter is not reset
3:3	iem_bit	RW	1	True	x00	1 = event input is enabled
2:2	irq_bit	RW	1	True	x00	1 = IRQ is enabled when counter ==cmp value
1:1	reset_bit	W1C	1	True	x00	1 = reset the counter
0:0	enable_bit	RW	1	True	x00	1 = enable the counter to count

## cfg_reg_hi - 0x4
1 = 64-bit mode, 0=32-bit mode
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:31	mode_64_bit	RW	1	True	x00	1 = 64-bit mode, 0=32-bit mode
30:30	mode_mtime_bit	RW	1	True	x00	1=MTIME mode Changes interrupt to be >= CMP value
14:8	prescaler_count	RW	7	True	x00	Prescaler divisor
7:7	ref_clk_en_bit	RW	1	True	x00	1= use Refclk for counter, 0 = use APB bus clk for counter
6:6	prescaler_en_bit	RW	1	True	x00	1= Use prescaler 0= no prescaler
5:5	one_shot_bit	RW	1	True	x00	1= disable timer when counter == cmp value
4:4	cmp_clr_bit	RW	1	True	x00	1=counter is reset once counter == cmp, 0=counter is not reset
3:3	iem_bit	RW	1	True	x00	1 = event input is enabled
2:2	irq_bit	RW	1	True	x00	1 = IRQ is enabled when counter ==cmp value
1:1	reset_bit	W1C	1	True	x00	1 = reset the counter
0:0	enable_bit	RW	1	True	x00	1 = enable the counter to count

## timer_val_lo - 0x8
32-bit counter value low 32-bits in 64-bit mode
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_val_lo	RW	32	False	x00	32-bit counter value low 32-bits in 64-bit mode

## timer_val_hi - 0xc
32-bit counter value high 32-bits in 64-bit mode
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_val_hi	RW	32	False	x00	32-bit counter value high 32-bits in 64-bit mode

## timer_cmp_lo - 0x10
compare value for low 32-bit counter
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_cmp_lo	RW	32	False	x00	compare value for low 32-bit counter

## timer_cmp_hi - 0x14
compare value for high 32-bit counter
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_cmp_hi	RW	32	False	x00	compare value for high 32-bit counter

## timer_start_lo - 0x18
Write strobe address for starting low counter
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_start_lo	WO	32	False	x00	Write strobe address for starting low counter

## timer_start_hi - 0x1c
Write strobe address for starting high counter
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_start_hi	WO	32	False	x00	Write strobe address for starting high counter

## timer_reset_lo - 0x20
Write strobe address for resetting the low counter
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_reset_lo	WO	32	False	x00	Write strobe address for resetting the low counter

## timer_reset_hi - 0x24
Write strobe address for resetting the high counter
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
31:0	timer_reset_hi	WO	32	False	x00	Write strobe address for resetting the high counter