cvmcu Chip DV Architecture Specifications

Generated 2023/12/6

Copyright 2023
Datum Technology Corporation
# Description
CORE-V-MCU
# Design Under Test
## Design Element
Name	Type	Source
core_v_mcu	fsoc	core-v-mcu

## Elaboration Parameters
Name	Type	Description
use_cores	bit	Includes the Core Sub-System

## Targets
### gf22fdx
Global Foundries 22nm FDX process
Name	Value
use_cores	1

### nexys
Nexys7
Name	Value
use_cores	1

### genesys
Genesys
Name	Value
use_cores	1

## Clocks
Name	Frequency	Signal Name	Description
sys_clk	100000000 Hz	ref_clk_i	System
jtag_clk	50000000 Hz	jtag_tck_i	JTAG

## Resets
Name	Clock	Signal Name	Description
sys_reset	sys_clk	rstn_i	System
jtag_reset	jtag_clk	jtag_trst_i	JTAG

## Probe Signals
Name	Direction	Size	Clock	Reset	Description
bootsel_i	in	1	sys_clk	sys_reset	Boot select
stm_i	in	1	sys_clk	sys_reset	Structural Test Mode

# Environment Configuration
Name	Type	Description
use_cores	bit	Includes the Core Sub-System

# Sub-System Environment Instances
## apb_timer
Simple timer
IP	Active/Passive	HDL Path
apb_timer	Passive	i_soc_domain.soc_peripherals_i.i_apb_timer_unit

## apb_adv_timer
Advanced timer (PWM)
IP	Active/Passive	HDL Path
apb_adv_timer	Passive	i_soc_domain.soc_peripherals_i.i_apb_adv_timer

# Agent Instances
## jtag
JTAG controller
IP	jtag
Active/Passive	Active
Mode	Normal
Clock	jtag_clk
Reset	sys_reset
Memory Map
HDL Path	jtag_{{ name }}_{{ dir }}

## qspi_s0
QSPI slave 0
IP	spi
Active/Passive	Active
Mode	Bypass -> io

### Configuration
Knob	Value
data_width	4

## qspi_s1
QSPI slave 1
IP	spi
Active/Passive	Active
Mode	Bypass -> io

### Configuration
Knob	Value
data_width	4

## camera
Camera Parallel Interface transmitter
IP	cvmcu_cpi
Active/Passive	Active
Mode	Bypass -> io

## i2c_s0
I2C slave 0
IP	i2c
Active/Passive	Active
Mode	Bypass -> io

## i2c_s1
I2C slave 1
IP	i2c
Active/Passive	Active
Mode	Bypass -> io

## uart0
UART 0
IP	uart
Active/Passive	Active
Mode	Bypass -> io

## uart1
UART 1
IP	uart
Active/Passive	Active
Mode	Bypass -> io

## sdio
Flash card
IP	sdio
Active/Passive	Active
Mode	Bypass -> io
Memory Map

## i2c_m
I2C master
IP	i2c
Active/Passive	Active
Mode	Bypass -> io

## io
IO ports
IP	cvmcu_io
Active/Passive	Active
Mode	Normal
Clock	sys_clk
Reset	sys_reset
HDL Path

## instr_obi
Instruction memory OBI
IP	obi
Active/Passive	Active
Mode	Normal
Clock	i_soc_domain.fc_subsystem_i.clk_i
Reset	i_soc_domain.fc_subsystem_i.rst_ni
Memory Map
HDL Path	i_soc_domain.fc_subsystem_i.core_instr_{{ name }}

### Configuration
Knob	Value
data_width	32
addr_width	32

## data_obi
Data memory OBI
IP	obi
Active/Passive	Active
Mode	Normal
Clock	i_soc_domain.fc_subsystem_i.clk_i
Reset	i_soc_domain.fc_subsystem_i.rst_ni
Memory Map	default
HDL Path	i_soc_domain.fc_subsystem_i.core_data_{{ name }}

### Configuration
Knob	Value
data_width	32
addr_width	32

## event
Event
IP	cvmcu_event
Active/Passive	Passive
Mode	Normal
Clock	i_soc_domain.soc_peripherals_i.clk_i
Reset	i_soc_domain.soc_peripherals_i.rst_ni
HDL Path	i_soc_domain.soc_peripherals_i.u_evnt_gen.{{ name }}

## dbg
Debug
IP	cvmcu_dbg
Active/Passive	Passive
Mode	Normal
Clock	i_soc_domain.fc_subsystem_i.clk_i
Reset	i_soc_domain.fc_subsystem_i.rst_ni
HDL Path	i_soc_domain.fc_subsystem_i.{{ name }}

# Prediction and Scoreboards
Path Name	Predictor Source (Expected)	Actual Source
apb_i2c_egress	sequencer: apb_i2c_egress_exp_ap	i2c_m agent: s2m_mon_trn_ap
apb_i2c_ingress	i2c_m agent: m2s_mon_trn_ap	sequencer: apb_i2c_ingress_act_ap
dbg	sequencer: dbg_exp_ap	dbg agent: mon_trn_ap
gpio_egress	sequencer: gpio_egress_exp_ap	io agent: eg_mon_trn_ap
gpio_ingress	io agent: ig_mon_trn_ap	sequencer: gpio_ingress_act_ap
udma_camera	camera agent: mon_trn_ap	sequencer: udma_camera_act_ap
udma_i2c0_egress	sequencer: udma_i2c0_egress_exp_ap	i2c_s0 agent: m2s_mon_trn_ap
udma_i2c0_ingress	i2c_s0 agent: s2m_mon_trn_ap	sequencer: udma_i2c0_ingress_act_ap
udma_i2c1_egress	sequencer: udma_i2c1_egress_exp_ap	i2c_s1 agent: m2s_mon_trn_ap
udma_i2c1_ingress	i2c_s1 agent: s2m_mon_trn_ap	sequencer: udma_i2c1_ingress_act_ap
udma_qspi0_egress	sequencer: udma_qspi0_egress_exp_ap	qspi_s0 agent: m2s_mon_trn_ap
udma_qspi0_ingress	qspi_s0 agent: s2m_mon_trn_ap	sequencer: udma_qspi0_ingress_act_ap
udma_qspi1_egress	sequencer: udma_qspi1_egress_exp_ap	qspi_s1 agent: m2s_mon_trn_ap
udma_qspi1_ingress	qspi_s1 agent: s2m_mon_trn_ap	sequencer: udma_qspi1_ingress_act_ap
udma_uart0_egress	sequencer: udma_uart0_egress_exp_ap	uart0 agent: eg_mon_trn_ap
udma_uart0_ingress	uart0 agent: ig_mon_trn_ap	sequencer: udma_uart0_ingress_act_ap
udma_uart1_egress	sequencer: udma_uart1_egress_exp_ap	uart1 agent: eg_mon_trn_ap
udma_uart1_ingress	uart1 agent: ig_mon_trn_ap	sequencer: udma_uart1_ingress_act_ap

# Sequences
## Init
Initializes any and all probe signals at start of simulation.
## Cfg
Sets register values to reflect environment configuration.
## uart_eg
Sequence for test 'uart_eg'.
### Knobs
Name	Type	Description
num_items	int unsigned	Number of transactions generated.
min_gap	int unsigned	Minimum cycles between transactions.
max_gap	int unsigned	Maximum cycles between transactions.

## uart_ig
Sequence for test 'uart_ig'.
### Knobs
Name	Type	Description
num_items	int unsigned	Number of transactions generated.
min_gap	int unsigned	Minimum cycles between transactions.
max_gap	int unsigned	Maximum cycles between transactions.

# Common Test Configuration Knobs
Name	CLI Arg	Type	Description
selected_reg_block	REG_BLOCK	Register Block	Register block selected for register testing.

# Tests
Note: Automated register tests (ex: reg_bit_bash) are omitted for brevity.
## Functional
### Uart
#### uart_eg
Generates UART transactions from the core towards the outside world
##### Goals
Scoreboard 'udma_uart0_egress' must observe 'num_items' matches.
Scoreboard 'udma_uart1_egress' must observe 'num_items' matches.
##### Knobs
Name	CLI Arg	Type	Description
num_items		int unsigned	Number of transactions generated.
min_gap		int unsigned	Minimum cycles between transactions.
max_gap		int unsigned	Maximum cycles between transactions.

##### Sequence Instances
Name	Type	Phase
uart_eg	uart_eg	main

##### Regression Entries
Target	Regression	[Seeds]/Count	Arguments
	sanitysanitysanity	[1]
	nightlynightlynightly	10
	weeklyweeklyweekly	100

#### uart_ig
Generates UART transactions from the outside world towards the core
##### Goals
Scoreboard 'udma_uart0_ingress' must observe 'num_items' matches.
Scoreboard 'udma_uart1_ingress' must observe 'num_items' matches.
##### Knobs
Name	CLI Arg	Type	Description
num_items		int unsigned	Number of transactions generated.
min_gap		int unsigned	Minimum cycles between transactions.
max_gap		int unsigned	Maximum cycles between transactions.

##### Sequence Instances
Name	Type	Phase
uart_ig	uart_ig	main

##### Regression Entries
Target	Regression	[Seeds]/Count	Arguments
	sanitysanitysanity	[1]
	nightlynightlynightly	10
	weeklyweeklyweekly	100