Interrupts Specifications

Generated 2023/12/8

Copyright 2023
Datum Technology Corporation
Chips
# cvmcu
CORE-V-MCU
## l1
First Level
Clock: fc_subsystem_i.clk_i
Reset: fc_subsystem_i.rst_ni
HDL Path: fc_subsystem_i.r_int
Name	Index	Description
CLINT_SW	3	CLINT Software Event
CLINT_TIMER	7	CLINT Timer Event
CLINT_EXT	11	CLINT External Event
TIMER_LO	16	CUSTOM FAST Timer_LO Event
TIMER_HI	17	CUSTOM FAST Timer HI Event
REF_CLK_RISE	18	CUSTOM FAST Reference Clock Rise Event
REF_CLK_FALL	19	CUSTOM FAST Reference Clock Fall Event
I2C	20	CUSTOM FAST I2C Event
ADV_TIMER_0	21	CUSTOM FAST Advanced-Timer Events0
ADV_TIMER_1	22	CUSTOM FAST Advanced-Timer Events1
ADV_TIMER_2	23	CUSTOM FAST Advanced-Timer Events2
ADV_TIMER_3	24	CUSTOM FAST Advanced-Timer Events3
EFPGA_0	25	CUSTOM FAST eFPGA Events0
EFPGA_1	26	CUSTOM FAST eFPGA Events1
EFPGA_2	27	CUSTOM FAST eFPGA Events2
EFPGA_3	28	CUSTOM FAST eFPGA Events3
EFPGA_4	29	CUSTOM FAST eFPGA Events4
EFPGA_5	30	CUSTOM FAST eFPGA Events5
ERROR	31	CUSTOM FAST Error Event

## l2
Platform-Specific (Second Level)
Clock: soc_peripherals_i.u_evnt_gen.u_arbiter.clk_i
Reset: soc_peripherals_i.u_evnt_gen.u_arbiter.rstn_i
HDL Path: soc_peripherals_i.u_evnt_gen.u_arbiter.grant_o
Name	Index	Description
UART0_0	0	UART-0 Event #0
UART0_1	1	UART-0 Event #1
UART0_2	2	UART-0 Event #2
UART0_3	3	UART-0 Event #3
UART1_0	4	UART-1 Event #0
UART1_1	5	UART-1 Event #1
UART1_2	6	UART-1 Event #2
UART1_3	7	UART-1 Event #3
QSPI0_0	8	QSPI-0 Event #0
QSPI0_1	9	QSPI-0 Event #1
QSPI0_2	10	QSPI-0 Event #2
QSPI0_3	11	QSPI-0 Event #3
QSPI1_0	12	QSPI-1 Event #0
QSPI1_1	13	QSPI-1 Event #1
QSPI1_2	14	QSPI-1 Event #2
QSPI1_3	15	QSPI-1 Event #3
I2C0_0	16	I2C-0 Event #0
I2C0_1	17	I2C-0 Event #1
I2C0_2	18	I2C-0 Event #2
I2C0_3	19	I2C-0 Event #3
I2C1_0	20	I2C-1 Event #0
I2C1_1	21	I2C-1 Event #1
I2C1_2	22	I2C-1 Event #2
I2C1_3	23	I2C-1 Event #3
SDIO_0	24	SDIO Event #0
SDIO_1	25	SDIO Event #1
SDIO_2	26	SDIO Event #2
SDIO_3	27	SDIO Event #3
CAMERA_0	28	Camera Event #0
CAMERA_1	29	Camera Event #1
CAMERA_2	30	Camera Event #2
CAMERA_3	31	Camera Event #3
FILTER_0	32	Filter Event #0
FILTER_1	33	Filter Event #1
FILTER_2	34	Filter Event #2
FILTER_3	35	Filter Event #3
EFPGA_0	112	eFPGA Event #0
EFPGA_1	113	eFPGA Event #1
EFPGA_2	114	eFPGA Event #2
EFPGA_3	115	eFPGA Event #3
EFPGA_4	116	eFPGA Event #4
EFPGA_5	117	eFPGA Event #5
EFPGA_6	118	eFPGA Event #6
EFPGA_7	119	eFPGA Event #7
EFPGA_8	120	eFPGA Event #8
EFPGA_9	121	eFPGA Event #9
EFPGA_10	122	eFPGA Event #10
EFPGA_11	123	eFPGA Event #11
EFPGA_12	124	eFPGA Event #12
EFPGA_13	125	eFPGA Event #13
EFPGA_14	126	eFPGA Event #14
EFPGA_15	127	eFPGA Event #15
GPIO_0	128	GPIO Event #0
GPIO_1	129	GPIO Event #1
GPIO_2	130	GPIO Event #2
GPIO_3	131	GPIO Event #3
GPIO_4	132	GPIO Event #4
GPIO_5	133	GPIO Event #5
GPIO_6	134	GPIO Event #6
GPIO_7	135	GPIO Event #7
GPIO_8	136	GPIO Event #8
GPIO_9	137	GPIO Event #9
GPIO_10	138	GPIO Event #10
GPIO_11	139	GPIO Event #11
GPIO_12	140	GPIO Event #12
GPIO_13	141	GPIO Event #13
GPIO_14	142	GPIO Event #14
GPIO_15	143	GPIO Event #15
GPIO_16	144	GPIO Event #16
GPIO_17	145	GPIO Event #17
GPIO_18	146	GPIO Event #18
GPIO_19	147	GPIO Event #19
GPIO_20	148	GPIO Event #20
GPIO_21	149	GPIO Event #21
GPIO_22	150	GPIO Event #22
GPIO_23	151	GPIO Event #23
GPIO_24	152	GPIO Event #24
GPIO_25	153	GPIO Event #25
GPIO_26	154	GPIO Event #26
GPIO_27	155	GPIO Event #27
GPIO_28	156	GPIO Event #28
GPIO_29	157	GPIO Event #29
GPIO_30	158	GPIO Event #30
GPIO_31	159	GPIO Event #31
APB_SW_0	160	APB Software Event #0
APB_SW_1	161	APB Software Event #1
APB_SW_2	162	APB Software Event #2
APB_SW_3	163	APB Software Event #3
APB_SW_4	164	APB Software Event #4
APB_SW_5	165	APB Software Event #5
APB_SW_6	166	APB Software Event #6
APB_SW_7	167	APB Software Event #7
REF_CLK_RISE	168	Reference Clock Rise Event

Sub-Systems
# apb_timer
APB simple timer unit
## events
Events
Clock: $sys_clk
Reset: $sys_reset
Name	HDL Path	Description
LOW	irq_lo_o	Low
HIGH	irq_hi_o	High

# apb_adv_timer
APB Advanced Timer
## events
Events
Clock: $sys_clk
Reset: $sys_reset
HDL Path: events_o
Name	Index	Description
EVENT_0	0	Event #0
EVENT_1	1	Event #1
EVENT_2	2	Event #2
EVENT_3	3	Event #3