cvmcu_dbg Agent DV Architecture Specifications

Generated 2023/12/8

Copyright 2023
Datum Technology Corporation
# Description
Type: Streaming simplex for parallel interface. Modes are 'core' & 'sys'
CORE-V-MCU Debug Interface

# Interface
## Clocks
Signal Name	Default Frequency	Type	Description
clk	100000000 Hz	SDR	Slow

## Reset
Signal Name	Clock	Description
reset_n	clk	System

## Modports
Name	Clock	Description
phy	clk	Physical

## Pins
Name	Modport	Driver	Width	Description
debug_req_i	phy	sys	1	Request input
stoptimer_o	phy	core	1	Timer stop output

# Enumerated Types
Name	Values
event_type / Event types	debug_req / stop_timer

# Sequence Item
## Randomized Fields
Name	Type	Description
event_type	uvma_cvmcu_dbg_event_type_enum	Event type

# Monitor Transaction
## Scoreboarded Fields
Name	Type	Description
event_type	uvma_cvmcu_dbg_event_type_enum	Event type

# Sequences
## Agent Sequences
### fix_stim
Generates fixed (reference) stimulus.
### rand_stim
Generates legal random stimulus with knobs for gap control.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

### fix_ill_stim
Generates a mix of legal and illegal fixed (reference) stimulus.
### rand_ill_stim
Generates a random mix of legal and illegal stimulus with knobs for gap control.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
num_errors	int unsigned	Number of errored sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

#### Fields
Name	Type	Description
error_idx_q	bit	Illegal sequence item indices.
error_count	int unsigned	Tally for illegal sequence items generated.

# Self-Testing

## Prediction and Scoreboarding
Path Name	Predictor Source (Expected)	Actual Source
agent	core_agent.seq_item_ap	passive_agent.mon_trn_ap
e2e	core_agent.mon_trn_ap	sys_agent.mon_trn_ap

## Common Test Configuration Knobs
Name	CLI Arg	Type	Description
num_items	NITEMSNITEMS	int unsigned	Number of sequence items to be generated.
min_gap	MINGMING	int unsigned	Minimum number of cycles between items.
max_gap	MAXGMAXG	int unsigned	Maximum number of cycles between items.
num_errors	NERRORSNERRORS	int unsigned	Number of errored sequence items to be generated.

## Tests
### Functional
#### Fix
##### fix_stim
Checks basic functionality with fixed valid stimulus and scoreboarding.
###### Goals
Scoreboard 'core_agent' must observe more than '0' matches.
Scoreboard 'sys_agent' must observe more than '0' matches.
Scoreboard '' must observe more than '0' matches.
Scoreboard '' must observe more than '0' matches.
###### Sequences
Name	Type	Phase
fix_stim	fix_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

#### Rand
##### rand_stim
Ensures functionality with random valid stimulus and synchronized scoreboarding.
###### Goals
Scoreboard 'core_agent' must observe 'test_cfg.num_items' matches.
Scoreboard 'sys_agent' must observe 'test_cfg.num_items' matches.
Scoreboard '' must observe 'test_cfg.num_items' matches.
Scoreboard '' must observe 'test_cfg.num_items' matches.
###### Sequences
Name	Type	Phase
rand_stim	rand_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10
nightly	10	NITEMS = 100
weekly	100	NITEMS = 1000

### Error
#### Fix
##### fix_ill_stim
Checks fault handling with fixed illegal stimulus and scoreboarding.
###### Goals
Scoreboard 'core_agent' must observe more than '0' matches.
Scoreboard 'sys_agent' must observe more than '0' matches.
Scoreboard '' must observe more than '0' matches.
Scoreboard '' must observe more than '0' matches.
###### Sequences
Name	Type	Phase
fix_ill_stim	fix_ill_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

#### Rand
##### rand_ill_stim
Ensures robustness with a mix of valid and illegal, random stimulus with synchronized scoreboarding.
###### Goals
Scoreboard 'core_agent' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard 'sys_agent' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard '' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard '' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
###### Sequences
Name	Type	Phase
rand_ill_stim	rand_ill_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10 / NERRORS = 1
nightly	10	NITEMS = 100 / NERRORS = 10
weekly	100	NITEMS = 1000 / NERRORS = 100