apb_adv_timer_ss Registers & Memories

Generated 2023/12/22

Copyright 2023
Datum Technology Corporation
# Parameters
Word size: 32
Endianness: little
# Registers
## t0_cmd - 0x0
ADV_TIMER0 start command bitfield.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
0:0	start	WO	1	False	x00	ADV_TIMER0 start command bitfield.
1:1	stop	WO	1	False	x00	ADV_TIMER0 stop command bitfield.
2:2	update	WO	1	False	x00	ADV_TIMER0 update command bitfield.
3:3	reset	WO	1	False	x00	ADV_TIMER0 reset command bitfield.
4:4	arm	WO	1	False	x00	ADV_TIMER0 arm command bitfield.
31:5	rfu	WO	27	False	x00

## t0_config - 0x4
ADV_TIMER0 input source configuration bitfield:
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
7:0	insel	RW	8	False	x00	ADV_TIMER0 input source configuration bitfield:
10:8	mode	RW	3	False	x00	ADV_TIMER0 trigger mode configuration bitfield:
11:11	clksel	RW	1	False	x00	ADV_TIMER0 clock source configuration bitfield:
12:12	updownsel	RW	1	False	x11	ADV_TIMER0 center-aligned mode configuration bitfield:
23:16	presc	RW	8	False	x00	ADV_TIMER0 prescaler value configuration bitfield.

## t0_threshold - 0x8
ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th_lo	RW	16	False	x00	ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
31:16	th_hi	RW	16	False	x00	ADV_TIMER0 threshold high part configuration bitfield. It defines end counter value.

## t0_th_channel0 - 0xc
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t0_th_channel1 - 0x10
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t0_th_channel2 - 0x14
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t0_th_channel3 - 0x18
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t0_counter - 0x2c
ADV_TIMER0 counter value.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	counter	WO	16	False	x00	ADV_TIMER0 counter value.

## t1_cmd - 0x40
ADV_TIMER0 start command bitfield.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
0:0	start	WO	1	False	x00	ADV_TIMER0 start command bitfield.
1:1	stop	WO	1	False	x00	ADV_TIMER0 stop command bitfield.
2:2	update	WO	1	False	x00	ADV_TIMER0 update command bitfield.
3:3	reset	WO	1	False	x00	ADV_TIMER0 reset command bitfield.
4:4	arm	WO	1	False	x00	ADV_TIMER0 arm command bitfield.
31:5	rfu	WO	27	False	x00

## t1_config - 0x44
ADV_TIMER0 input source configuration bitfield:
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
7:0	insel	RW	8	False	x00	ADV_TIMER0 input source configuration bitfield:
10:8	mode	RW	3	False	x00	ADV_TIMER0 trigger mode configuration bitfield:
11:11	clksel	RW	1	False	x00	ADV_TIMER0 clock source configuration bitfield:
12:12	updownsel	RW	1	False	x11	ADV_TIMER0 center-aligned mode configuration bitfield:
23:16	presc	RW	8	False	x00	ADV_TIMER0 prescaler value configuration bitfield.

## t1_threshold - 0x48
ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th_lo	RW	16	False	x00	ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
31:16	th_hi	RW	16	False	x00	ADV_TIMER0 threshold high part configuration bitfield. It defines end counter value.

## t1_th_channel0 - 0x4c
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t1_th_channel1 - 0x50
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t1_th_channel2 - 0x54
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t1_th_channel3 - 0x58
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t1_counter - 0x6c
ADV_TIMER0 counter value.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	counter	WO	16	False	x00	ADV_TIMER0 counter value.

## t2_cmd - 0x80
ADV_TIMER0 start command bitfield.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
0:0	start	WO	1	False	x00	ADV_TIMER0 start command bitfield.
1:1	stop	WO	1	False	x00	ADV_TIMER0 stop command bitfield.
2:2	update	WO	1	False	x00	ADV_TIMER0 update command bitfield.
3:3	reset	WO	1	False	x00	ADV_TIMER0 reset command bitfield.
4:4	arm	WO	1	False	x00	ADV_TIMER0 arm command bitfield.
31:5	rfu	WO	27	False	x00

## t2_config - 0x84
ADV_TIMER0 input source configuration bitfield:
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
7:0	insel	RW	8	False	x00	ADV_TIMER0 input source configuration bitfield:
10:8	mode	RW	3	False	x00	ADV_TIMER0 trigger mode configuration bitfield:
11:11	clksel	RW	1	False	x00	ADV_TIMER0 clock source configuration bitfield:
12:12	updownsel	RW	1	False	x11	ADV_TIMER0 center-aligned mode configuration bitfield:
23:16	presc	RW	8	False	x00	ADV_TIMER0 prescaler value configuration bitfield.

## t2_threshold - 0x88
ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th_lo	RW	16	False	x00	ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
31:16	th_hi	RW	16	False	x00	ADV_TIMER0 threshold high part configuration bitfield. It defines end counter value.

## t2_th_channel0 - 0x8c
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t2_th_channel1 - 0x90
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t2_th_channel2 - 0x94
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t2_th_channel3 - 0x98
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t2_counter - 0xac
ADV_TIMER0 counter value.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	counter	WO	16	False	x00	ADV_TIMER0 counter value.

## t3_cmd - 0xc0
ADV_TIMER0 start command bitfield.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
0:0	start	WO	1	False	x00	ADV_TIMER0 start command bitfield.
1:1	stop	WO	1	False	x00	ADV_TIMER0 stop command bitfield.
2:2	update	WO	1	False	x00	ADV_TIMER0 update command bitfield.
3:3	reset	WO	1	False	x00	ADV_TIMER0 reset command bitfield.
4:4	arm	WO	1	False	x00	ADV_TIMER0 arm command bitfield.
31:5	rfu	WO	27	False	x00

## t3_config - 0xc4
ADV_TIMER0 input source configuration bitfield:
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
7:0	insel	RW	8	False	x00	ADV_TIMER0 input source configuration bitfield:
10:8	mode	RW	3	False	x00	ADV_TIMER0 trigger mode configuration bitfield:
11:11	clksel	RW	1	False	x00	ADV_TIMER0 clock source configuration bitfield:
12:12	updownsel	RW	1	False	x11	ADV_TIMER0 center-aligned mode configuration bitfield:
23:16	presc	RW	8	False	x00	ADV_TIMER0 prescaler value configuration bitfield.

## t3_threshold - 0xc8
ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th_lo	RW	16	False	x00	ADV_TIMER0 threshold low part configuration bitfield. It defines start counter value.
31:16	th_hi	RW	16	False	x00	ADV_TIMER0 threshold high part configuration bitfield. It defines end counter value.

## t3_th_channel0 - 0xcc
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t3_th_channel1 - 0xd0
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t3_th_channel2 - 0xd4
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t3_th_channel3 - 0xd8
ADV_TIMER0 channel 0 threshold configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	th	RW	16	False	x00	ADV_TIMER0 channel 0 threshold configuration bitfield.
18:16	mode	RW	3	False	x00	ADV_TIMER0 channel 0 threshold match action on channel output signal configuration bitfield:

## t3_counter - 0xec
ADV_TIMER0 counter value.
Type: WO
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
15:0	counter	WO	16	False	x00	ADV_TIMER0 counter value.

## event_cfg - 0x100
ADV_TIMER output event 0 source configuration bitfiled:
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
3:0	sel0	RW	4	False	x00	ADV_TIMER output event 0 source configuration bitfiled:
7:4	sel1	RW	4	False	x00	ADV_TIMER output event 1 source configuration bitfiled:
11:8	sel2	RW	4	False	x00	ADV_TIMER output event 2 source configuration bitfiled:
15:12	sel3	RW	4	False	x00	ADV_TIMER output event 3 source configuration bitfiled:
19:16	ena	RW	4	False	x00	ADV_TIMER output event enable configuration bitfield. ENA[i]=1 enables output event i generation.

## cg - 0x104
ADV_TIMER clock gating configuration bitfield.
Type: RW
Volatile: False
HDL Path:
Bits	Name	R/W	Size	Volatile	Reset	Description
3:0	ena	RW	4	False	x00	ADV_TIMER clock gating configuration bitfield.