apb_timer Sub-System DV Architecture Specifications

Generated 2023/12/22

Copyright 2023
Datum Technology Corporation

# Description
APB simple timer unit
# Design Under Test
## Design Element
Name	Type	Source
apb_timer_unit	fsoc	core-v-mcu

## Clocks
Name	Frequency	Signal Name	Description
sys_clk	100000000 Hz	HCLK	Processor
ref_clk	32000 Hz	ref_clk_i	Reference

## Resets
Name	Clock	Signal Name	Description
sys_reset	sys_clk	HRESETn	System

## Probe Signals
Name	Direction	Size	Clock	Reset	Description
stoptimer_i	in	1	sys_clk	sys_reset	Stop timer input
event_lo_i	in	1	sys_clk	sys_reset	Event low input
event_hi_i	in	1	sys_clk	sys_reset	Event high input
busy_o	out	1	sys_clk	sys_reset	Busy output

# Block Environment Instances
## counter_lo
Counter block 0
IP	Active/Passive	HDL Path
tcounter	Passive	counter_lo_i

## counter_hi
Counter block 1
IP	Active/Passive	HDL Path
tcounter	Passive	counter_hi_i

## prescaler_lo
Prescaler block 0
IP	Active/Passive	HDL Path
tprescaler	Passive	prescaler_lo_i

## prescaler_hi
Prescaler block 1
IP	Active/Passive	HDL Path
tprescaler	Passive	prescaler_hi_i

# Agent Instances
## proc
Processor interface
IP	apb
Active/Passive	Active
Mode	Normal
Clock	sys_clk
Reset	sys_reset
Memory Map	default
HDL Path	{{ name.upper() }}

### Configuration
Knob	Value
data_width	32
addr_width	32

# Common Test Configuration Knobs
Name	CLI Arg	Type	Description
selected_reg_block	REG_BLOCK	Register Block	Register block selected for register testing.

# Tests
Note: Automated register tests (ex: reg_bit_bash) are omitted for brevity.