cvmcu_io Agent DV Architecture Specifications

Generated 2023/12/6

Copyright 2023
Datum Technology Corporation
# Description
Type: Streaming full-duplex for parallel interface. Modes are 'board' & 'chip' and directions are 'ig' & 'eg'.
CORE-V-MCU IO

# Interface
## Clocks
Signal Name	Default Frequency	Type	Description
ref_clk_i	100000000 Hz	SDR	Reference Clock

## Reset
Signal Name	Clock	Description
rstn_i	ref_clk_i	Active-low asynchronous reset

## Modports
Name	Clock	Description
padi	ref_clk_i	PAD input
pado	ref_clk_i	PAD output

## Pins
Name	Modport	Driver	Width	Description
io_in_i	padi	board	48	Port’s input signal
io_out_o	pado	chip	48	Port's output signal
pad_cfg_o	pado	chip	[48][6]	PAD configuration (implementation dependent)
io_oe_o	pado	chip	48	Port’s Output Enable 1: IO = io_out_o. 0: io_in_i = IO.
slow_clk_o	pado	chip	1	Output clock generated from ref_clk_i. Frequency is implementation dependent.

# Sequence Item
# Monitor Transaction
# Sequences
## Agent Sequences
### fix_stim
Generates fixed (reference) stimulus.
### rand_stim
Generates legal random stimulus with knobs for gap control.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

### fix_ill_stim
Generates a mix of legal and illegal fixed (reference) stimulus.
### rand_ill_stim
Generates a random mix of legal and illegal stimulus with knobs for gap control.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
num_errors	int unsigned	Number of errored sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

#### Fields
Name	Type	Description
error_idx_q	bit	Illegal sequence item indices.
error_count	int unsigned	Tally for illegal sequence items generated.

# Self-Testing

## Prediction and Scoreboarding
Path Name	Predictor Source (Expected)	Actual Source
board	board_agent.seq_item_ap	passive_agent.ig_mon_trn_ap
chip	chip_agent.seq_item_ap	passive_agent.eg_mon_trn_ap
ig	board_agent.ig_mon_trn_ap	chip_agent.ig_mon_trn_ap
eg	chip_agent.eg_mon_trn_ap	board_agent.eg_mon_trn_ap

## Environment Sequences
### fix_stim
Sequence for test 'fix_stim'.
#### Sub-Sequence Instances
Name	Type
board	fix_stim
chip	fix_stim

### rand_stim
Sequence for test 'rand_stim'.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

#### Sub-Sequence Instances
Name	Type
board	rand_stim
chip	rand_stim

### fix_ill_stim
Sequence for test 'fix_ill_stim'.
#### Sub-Sequence Instances
Name	Type
board	fix_ill_stim
chip	fix_ill_stim

### rand_ill_stim
Sequence for test 'rand_ill_stim'.
#### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
num_errors	int unsigned	Number of errored sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

#### Sub-Sequence Instances
Name	Type
board	rand_ill_stim
chip	rand_ill_stim

## Common Test Configuration Knobs
Name	CLI Arg	Type	Description
num_items	NITEMSNITEMS	int unsigned	Number of sequence items to be generated.
min_gap	MINGMING	int unsigned	Minimum number of cycles between items.
max_gap	MAXGMAXG	int unsigned	Maximum number of cycles between items.
num_errors	NERRORSNERRORS	int unsigned	Number of errored sequence items to be generated.

## Tests
### Functional
#### Fix
##### fix_stim
Checks basic functionality with fixed valid stimulus and scoreboarding.
###### Goals
Scoreboard 'board_agent' must observe more than '0' matches.
Scoreboard 'chip_agent' must observe more than '0' matches.
Scoreboard 'ig' must observe more than '0' matches.
Scoreboard 'eg' must observe more than '0' matches.
###### Sequences
Name	Type	Phase
fix_stim	fix_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

#### Rand
##### rand_stim
Ensures functionality with random valid stimulus and synchronized scoreboarding.
###### Goals
Scoreboard 'board_agent' must observe 'test_cfg.num_items' matches.
Scoreboard 'chip_agent' must observe 'test_cfg.num_items' matches.
Scoreboard 'ig' must observe 'test_cfg.num_items' matches.
Scoreboard 'eg' must observe 'test_cfg.num_items' matches.
###### Sequences
Name	Type	Phase
rand_stim	rand_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10
nightly	10	NITEMS = 100
weekly	100	NITEMS = 1000

### Error
#### Fix
##### fix_ill_stim
Checks fault handling with fixed illegal stimulus and scoreboarding.
###### Goals
Scoreboard 'board_agent' must observe more than '0' matches.
Scoreboard 'chip_agent' must observe more than '0' matches.
Scoreboard 'ig' must observe more than '0' matches.
Scoreboard 'eg' must observe more than '0' matches.
###### Sequences
Name	Type	Phase
fix_ill_stim	fix_ill_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

#### Rand
##### rand_ill_stim
Ensures robustness with a mix of valid and illegal, random stimulus with synchronized scoreboarding.
###### Goals
Scoreboard 'board_agent' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard 'chip_agent' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard 'ig' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
Scoreboard 'eg' must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
###### Sequences
Name	Type	Phase
rand_ill_stim	rand_ill_stim	main

###### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10 / NERRORS = 1
nightly	10	NITEMS = 100 / NERRORS = 10
weekly	100	NITEMS = 1000 / NERRORS = 100