tprescaler Block DV Architecture Specifications

Generated 2023/12/12

Copyright 2023
Datum Technology Corporation
# Description
Timer unit prescaler
# Design Under Test
## Design Element
Name	Type	Source
timer_unit_counter_presc	fsoc	core-v-mcu

## Clocks
Signal Name	Default Frequency	Type	Description
clk_i	100000000 Hz	SDRSDR

## Reset
Signal Name	Clock	Description
rst_ni	clk_i

# Interface
## Modports
Name	Clock	Description
cp	clk_i	Control Plane
dpi	clk_i	Data Plane In
dpo	clk_i	Data Plane Out

## Pins
Name	Modport	Direction	Width	Description
reset_count_i	cp	in	1
enable_count_i	cp	in	1
compare_value_i	cp	in	32
write_counter_i	dpi	in	1
counter_value_i	dpi	in	32
counter_value_o	dpo	out	32
target_reached_o	dpo	out	1

# Sequence Item
# Monitor Transaction
# Prediction and Scoreboarding

# Environment Sequences
## fix_stim
Sequence for test 'fix_stim'.
## rand_stim
Sequence for test 'rand_stim'.
### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

## fix_ill_stim
Sequence for test 'fix_ill_stim'.
## rand_ill_stim
Sequence for test 'rand_ill_stim'.
### Knobs
Name	Type	Description
num_items	int unsigned	Number of sequence items to be generated.
num_errors	int unsigned	Number of errored sequence items to be generated.
min_gap	int unsigned	Minimum number of cycles between items.
max_gap	int unsigned	Maximum number of cycles between items.

### Fields
Name	Type	Description
error_idx_q	bit	Illegal sequence item indices.
error_count	int unsigned	Tally for illegal sequence items generated.

# Common Test Configuration Knobs
Name	CLI Arg	Type	Description
num_items	NITEMS	int unsigned	Number of sequence items to be generated.
min_gap	MING	int unsigned	Minimum number of cycles between items.
max_gap	MAXG	int unsigned	Maximum number of cycles between items.
num_errors	NERRORS	int unsigned	Number of errored sequence items to be generated.

# Tests
## Functional
### Fix
#### fix_stim
Checks basic functionality with fixed valid stimulus and scoreboarding.
##### Goals
Scoreboard must observe more than '0' matches.
##### Sequence Instances
Name	Type	Phase
fix_stim	fix_stim	main

##### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

### Rand
#### rand_stim
Ensures functionality with random valid stimulus and synchronized scoreboarding.
##### Goals
Scoreboard must observe 'test_cfg.num_items' matches.
##### Sequence Instances
Name	Type	Phase
rand_stim	rand_stim	main

##### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10
nightly	10	NITEMS = 100
weekly	100	NITEMS = 1000

## Error
### Fix
#### fix_ill_stim
Checks fault handling with fixed illegal stimulus and scoreboarding.
##### Goals
Scoreboard must observe more than '0' matches.
##### Sequence Instances
Name	Type	Phase
fix_ill_stim	fix_ill_stim	main

##### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]
nightly	[1]
weekly	[1]

### Rand
#### rand_ill_stim
Ensures robustness with a mix of valid and illegal, random stimulus with synchronized scoreboarding.
##### Goals
Scoreboard must observe '(test_cfg.num_items-test_cfg.num_errors)' matches.
##### Sequence Instances
Name	Type	Phase
rand_ill_stim	rand_ill_stim	main

##### Regression Entries
Regression	[Seeds]/Count	Arguments
sanity	[1]	NITEMS = 10 / NERRORS = 1
nightly	10	NITEMS = 100 / NERRORS = 10
weekly	100	NITEMS = 1000 / NERRORS = 100